## Slide 1
Multispectral Image Clustering and Compression with Kohonen SOM
GNR 602
Hrishikesh Lal Baishya (23b0743)

## Slide 2
Task
Cluster a multispectral image using Kohonen Self-Organizing Map, with user-specified grid matrix size. Compute the mean-squared-error between the input image and the decoded image when the SOM is used as an image compressor by varying the grid size.

## Slide 3
Introduction to Multispectral Imaging
What is it ?
Images captured at 3 to 15 spectral bands beyond visible RGB.
Key Applications
  Remote sensing
  Agricultural monitoring
  Environmental analysis
Data Structure
3D data cube: spatial (x,y) plus spectral dimensions.

## Slide 4
What It Does | How It Works
Performs unsupervised learning for clustering and visualization | Initialize weights for each node
Reduces dimensionality of high-dimensional data | Iterative weight adjustment
Transforms data into a 2D grid-based map | Update BMU & neighbors' weights using learning rate and distance
Preserves topological properties of the input space | Repeat over multiple iterations for convergence
Kohonen Self-Organizing Map Overview

## Slide 6
Methodology: SOM Clustering of Multispectral Image
Data Preparation
Normalize and standardize input multispectral data cube.
SOM Setup
Initialize using random weights.
Grid Sizes
Test 4x4, 8x8, 12x12, 16x16, 20x20 user-specified maps
Training
Set learning rate, neighborhood radius, and iterations

## Slide 7
Methodology: Data Preparation
Band Selection
  Downloaded TIFF images from the Copernicus Open Access Hub
  Selected four key spectral bands:
    Red (B4)
    Green (B3)
    Blue (B2)
    Near Infrared (NIR, B8)
    Focused on Sentinel data for high spatial and spectral resolution
  Combined individual bands to form a multispectral image stack
  Aligned bands spatially using georeferencing metadata
  Created a single 4-channel array for unified analysis
Image Stacking
Preprocessing
  Clipped images to Area of Interest (AOI)
  Applied cloud masking
  Normalized pixel values for consistent feature scaling
  Stored processed data for further feature extraction or classification

## Slide 8
Red Band
Green Band
Blue Band
NIR Band
Multispectral

## Slide 9
Methodology: SOM Setup & Training
Set grid size, input dimensions, learning rate, and initialize random weights
Initialization (__init__)
Winner Selection (winner)
Find Best Matching Unit (BMU) with minimum Euclidean distance to input
Neighborhood Function
Training & Mapping
Compute influence of BMU using Gaussian decay, reduces over time
Iteratively update BMU and neighboring weights; map each input to its BMU for visualization

## Slide 10
Results: Compressed Position Cluster

## Slide 11
Results: Codebook for different sizes after training

## Slide 12
Results : Reconstructed Images from weights

## Slide 13
Results: Reconstructed Bands from weights

## Slide 14
Results: Decompressed Images from weights

## Slide 15
  MSE decreases as grid size increases initially.
  Best performance (lowest MSE) observed at grid size = 256 nodes.
  Beyond 256 nodes, MSE slightly increases, indicating diminishing returns or possible overfitting.
Results: MSE v/s Total Nodes

## Slide 16
Thank you